## Slide 1
MFEM-Based Tokamak Equilibrium Solver
Students: Saisruthi Bandla (sbandla3@gatech.edu), Janani Murugan (janani@gatech.edu), Alex de Magalhaes
Mentors: Qi Tang, Assistant Professor at CSE
Project Goal: Develop a free boundary tokamak equilibrium solver for the magnetic confinement fusion community
Stabilize plasma and avoid contact with walls
Modeled by the Grad–Shafranov (GS) equation, which describes magnetohydrodynamic equilibria in axisymmetric, toroidal plasmas
Unknown plasma shape & boundary conditions
Modeled using MFEM (mfem.org), an open-source finite element library for solving partial differential equations on unstructured and adaptive meshes
Tokamak: Device for magnetic confinement fusion
Toroidal plasma chamber of tokamak
Solution simulation via MFEM
Plasma inside the toroidal chamber
Magnetic coils
Toroidal chamber and first wall
Generate a standard rectangular mesh and interpolate the solution onto it
Current Work: Using G-EQDSK file format, develop and integrate an EFIT writer (code used to reconstruct plasma equilibrium solutions) into MFEM
Identify and isolate the plasma region
Build EFIT writer
Compute additional necessary values
Output the metrics, with proper GEQDSK formation, to an exportable text file
Delivers a structured, portable set of key parameters for reproducing plasma equilibrium solutions, aligned with industry standards for easy sharing and integration
Plasma fusion: the process of charged particles colliding to releases energy
Benefits
Low-impact energy generation
Faster and longer-distance space travel
Scientific studies
Challenges
Develop devices that can contain and withstand high temperatures
Plasma expands and cools—need to stabilize to keeps it hot and long enough for fusion
Ongoing Efforts
Magnetic Confinement: Trap plasma with strong magnetic fields
Inertial Confinement: Uses lasers/beams for rapid compression of particles
State of the Art
Equilibrium solution on default triangular mesh
Gather the needed EFIT parameters from MFEM
Computational grid
Magnetic axis
Plasma state
Plasma boundary
Poloidal current and flux
Safety factor
Limiter grid
Future Work
Equilibrium
Free Boundary
Continue development of ITER tokamak solutions
Expand to other tokamaks
Test the GEQDSK file for potential errors
https://github.com/tangqi/mfem/tree/tds-gs/miniapps/gslib